## Slide 1: DICOM WG 30 Small Animal Imaging DICOM Training Enhanced Multi-frame & Quantitation
David Clunie (dclunie@dclunie.com)
PixelMed Publishing

## Slide 2: Learning Objectives
Background of DICOM IODs for storage
“Enhanced Multi-frame” family of objects – principles
Performance, compression, organization, attributes
Geometry, coded anatomy, hanging, timing, data type
Functional groups, dimensions, stack, temporal index
Real world value maps and display pipeline
PACS support for Enhanced Multi-frame
Legacy conversion
Quantitation and DICOM non-image objects for ROIs

## Slide 3: DICOM IOD History – CT/MR/PT
Single slice per instance (file)
  organized into “series”
  usually one “acquisition” per series
  many technique attributes optional/undefined
  proliferation of private attributes
  no dependency on protocol (e.g., anatomy)
  arose from pre-DICOM practice
Enhanced Multi-frame MR, CT and PET
  faster (?)
  easier (one instance or file per “acquisition”)
  better (information – commonality exposed)

## Slide 4: DICOM US IOD History
1993 original DICOM Standard
  contained ultrasound IODs
  single and multi-frame
  quickly retired
1995 Sup 5 Ultrasound
  what is currently used – single and multi-frame
2009 Sup 43 3D Ultrasound
  long time coming – effort started in 2002
  difficulty reaching consensus on scope/complexity
  3D and 4D Cartesian volumes (+/- time)
  “enhanced” family object

## Slide 5: Enhanced Family of Images
Enhanced MR Image – Sup 49
Enhanced US Volume – Sup 43
Revised Secondary Capture – Sup 57 + CP 600
Enhanced CT Image – Sup 58
Enhanced XA/XRF – Sup 83
Segmentation – Sup 111
X-Ray 3D – Sup 116
Enhanced PET – Sup 117
Breast Tomosynthesis – Sup 125
Whole Slide Microscopic Image – Sup 145
Intravascular OCT – Sup 151
Breast Projection X-Ray – Sup 165

## Slide 6: Performance Opportunities
New multi-frame object does not change
  TCP connection and Association establishment
Common header information is not repeated
  transfer reduction negligible compared to pixel data size
  parsing reduction time may be significant
Reduced latency (delay)
  between storage requests
Fewer database insertions
  one entry in image table versus one per slice
Creates opportunity for inter-slice compression
  3D or motion
  entire volume or slabs of sufficient size
Extremely implementation-dependent

## Slide 7: Factor Out Shared Attributes
Per-frame attributes
Pixel data
Shared attributes

## Slide 8
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
A s s o c i a t i o n

## Slide 9
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
UIDs
Store, parse, check
A s s o c i a t i o n
DB

## Slide 10
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
UIDs
Store, parse, check
A s s o c i a t i o n
DB
DB

## Slide 11
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
UIDs
Store, parse, check
A s s o c i a t i o n
DB
DB
DB

## Slide 12
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
UIDs
Store, parse, check
A s s o c i a t i o n
DB
DB
DB
DB

## Slide 14
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1

## Slide 15
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
1 mm
2

## Slide 16
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
1 mm
2
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
1 mm
1897
Potentially thousands of individual per slice database insertion operations

## Slide 17
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
1 mm
2
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
1 mm
1897
Potentially thousands of individual per slice database insertion operations

## Slide 18
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
Single database insertion - just don’t need per-slice detail in database

## Slide 19: Multi-frame compression
“Old” single frame SOP Classes
  compression only possible within a single frame
  lossless - typically 3:1 or 4:1 for CT and MR
Multi-frame objects
  take advantage of redundancy between frames
  spatial redundancy - JPEG 2000 Part 2
    lossless gain modest, lossy gain more substantial
  motion prediction - MPEG-2 and others
  new schemes - H.264/MPEG-4 Part 10
  entire dataset (e.g., 3D volume) or adjacent slabs

## Slide 20: Single Frame Lossless

## Slide 21: Single Frame Lossless

## Slide 26: Not (just) about performance
Greater “inter-functionality”
  browsing
  routing
  hanging
  rendering
Achieved through
  better description of organization of data
  more mandatory attributes
  more standard values (& codes)
  reduced dependence on private attributes

## Slide 27: Coded anatomic regions
Original SOP Classes
  incomplete list of optional defined terms
  US at least had optional coded anatomy (unlike CT)
  optional laterality
Enhanced SOP Classes
  mandatory coded anatomic region
  comprehensive & appropriate list of codes
  mandatory laterality
  per-frame or for entire object
E.g.
  (T-D3000,SRT,“Chest”)
  rather than free text “CHEST”, etc.

## Slide 28: CT Image Type Value 3
Original SOP Classes
  AXIAL or LOCALIZER
Enhanced SOP Classes
  common to CT and MR
    ANGIO, FLUOROSCOPY, LOCALIZER, MOTION, PERFUSION, PRE_CONTRAST, POST_CONTRAST, REST, STRESS, VOLUME
  CT-specific
    ATTENUATION, CARDIAC, CARDIAC_GATED, REFERENCE

## Slide 29: MR Acquisition Contrast
Original SOP Classes
  guess from echo and repetition time, etc.
  recognize proprietary Protocol Name
Enhanced SOP Classes
  new mandatory frame level attribute
  Acquisition Contrast
    DIFFUSION, FLOW_ENCODED, FLUID_ATTENUATED, PERFUSION, PROTON_DENSITY, STIR, TAGGING, T1, T2, T2_STAR, TOF

## Slide 30: Enhanced Contrast/Bolus
Original SOP Classes
  plain text description
  difficult to determine presence/absence
    e.g., description value of “None”
  single agent (did not distinguish oral/iv)
  codes optional and never used
Enhanced SOP Classes
  mandatory codes only
  multiple items with separate coded routes & timing
  presence or absence per-frame can be described

## Slide 31: Technique Attributes & Terms
 | CT |  | MR | 
SOP Class | Original | Enhanced | Original | Enhanced
Attributes (Mandatory) | 18 (0) | 41 (39) | 44 (2) | 103 (94)
Terms (Enumerated) | 4 (2) | 86 (18) | 38 (9) | 228 (47)

## Slide 32: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD

## Slide 33: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1

## Slide 34: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1

## Slide 35: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 0\1\0\0\0\-1

## Slide 36: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 0\1\0\0\0\-1

## Slide 37: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 0\1\0\0\0\-1
Contrast Agent #1
Administered = NO
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 38: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 0\1\0\0\0\-1
Contrast Agent #1
Administered = NO
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 39: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 1\0\0\0\1\0
Contrast Agent #1
Administered = NO
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 40: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 1\0\0\0\1\0
Contrast Agent #1
Administered = NO
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 41: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 1\0\0\0\1\0
Contrast Agent #1
Administered = NO
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 42: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T2
Image Orientation ≈ 1\0\0\0\1\0

## Slide 43: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T2
Image Orientation ≈ 1\0\0\0\1\0

## Slide 44: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T2
Image Orientation ≈ 1\0\0\0\1\0

## Slide 45: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 1\0\0\0\1\0
Contrast Agent #1
Administered = YES
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 46: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 1\0\0\0\1\0
Contrast Agent #1
Administered = YES
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 47: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD

## Slide 48: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Same rules, independent of whether:
one single multi-frame image
one multi-frame image per acquisition
one slice per single frame image
one series or multiple

## Slide 49: Hanging Protocol Support
A productivity advantage of the enhanced objects
Should not have to tailor hanging protocol rules to specific vendors or devices or versions
Reliable and standard information
  mandatory and standard places (attributes)
  mandatory and standard values
As technology evolves, yet more standard values are added to the DICOM standard
Eliminate dependence on site configured Series Number or Series Description, whether pre-populated from acquisition protocol or manually typed by operator
Not dependent on DICOM Hanging Protocol IOD

## Slide 50: Geometry Unchanged
Same as original SOP Classes
Image Position and Orientation (Patient)
Still need to compute AXIAL, SAGITTAL or CORONAL from orientation vector
Still need to compute edge labels (A/P etc) from orientation vector
May still need to compare orientation vectors to determine if slices are parallel, but Dimensions minimize the burden
For US Volume, new (Volume) vs. (Patient)

## Slide 51: Acquisition Timing Information
Original SOP Classes
  inconsistent use of
    Content (Image) Time
    Acquisition Time
    Frame Time (+/- Frame Time Vector)
  contrast timing information never used
Enhanced SOP Classes
  unambiguous definition of acquisition timing
  explicit relationships with contrast & cardiac timing

## Slide 52: Timing Information

## Slide 53: Cardiac Timing Information

## Slide 54: Organizational Features
Shared and Per-frame Functional Groups
  a Functional Group has Attributes that vary as a group
  e.g., Pixel Measures, Plane Orientation
  compact & makes explicit what doesn’t change
Dimensions
  a priori hints as to how the frames are organized
  specify intended order of traversal, such as space, then time (e.g., for cardiac cine loops)
Stacks
  groups of spatially-related slices, repeatable
Temporal positions
  “time slots” or “bins”

## Slide 55: Organizational Features
Goal is to reduce the work that the receiving application has to do to “figure out”
  how the data is organized
  why it is organized that way
Without preventing use of the data in unanticipated ways
  e.g. 3D on a dataset not intended as a volume
Two “levels”
  detailed: shared & per-frame attributes
  overall: dimensions, stacks and temporal positions

## Slide 56: Multi-frame Functional Groups
Per-frame attributes
Pixel data
Shared attributes

## Slide 57: What is a Functional Group?
“A set of logically related Attributes that are likely to vary together”
Examples:
  position related
  orientation related
  spacing related
  timing related
May be “shared” (all same) or “per-frame”
  Shared Functional Group Sequence – one item
  Per-Frame FGS – one item per frame (vector)

## Slide 58: Functional Group Encoding

## Slide 59: Compared to the “old way”
Frame Increment Pointer (used previously)
  m values, where m is number of varying attributes
  each value is tag of an attribute
  each attribute pointed to has n values (n frames)
  special case is Frame Time, which has just one value applicable to all frames
  otherwise, no commonality factored out
Used in
  “old” US Multi-frame, XA/XRF IODs for cine
  still used in NM (no enhanced version yet)
Not used in Enhanced family of IODs
  -> Per Frame Functional Group Sequence (CP 1260)

## Slide 60: Functional Groups – Varieties
Common to many IODs, e.g.,
  Pixel Measures
  Frame Anatomy
  Frame VOI LUT
  Real World Value Mapping
Specific to particular IODs, e.g.,
  MR Spatial Saturation
  CT Table Dynamics
  X-Ray Field of View
  PET Frame Correction Factors
  US Image Description

## Slide 61: Modules vs. Functional Groups
Still have traditional “Modules” at top level
Modules
  Attributes describing entire acquisition
  e.g., cumulative stuff
Shared functional groups
  Attributes about frames that happen to have the same values for all frames
Per-frame functional groups
  Attributes about frames that have different values for any frame

## Slide 62: Stacks
H\

## Slide 63
5
Stack ID
In-Stack Position
1
3
4
1
2
3
4
2
5

## Slide 64: Multi-frame Dimensions
Real world (Wikipedia):
  “In physics and mathematics, the dimension of a space or object is informally defined as
    the minimum number of coordinates needed to specify any point within it”
DICOM:
  “A dimension is a set of attributes
    that change on a per-frame basis in a manner that is known before the image is acquired,
    are defined by the generating application and
    are especially intended for presentation”

## Slide 65: Multi-frame Dimensions
Multi-frame Dimensions Module
  in top level dataset
  defines an “organization” (set of dimensions)
    with an optional organization “type”
    e.g., “3D” or “3D_TEMPORAL” in Volume US
  defines each dimension
    by reference to a per-frame varying Attribute
    by referenced to Functional Group containing Attribute
For each frame, encode
  numeric “index” of position within each dimension
    starts from 1, increases by 1
    an index, not the value of the referenced Attribute

## Slide 66: Dimensions
Space
5
In-Stack Position
Stack ID = 1
4
3
2
1
Start with a dimension of space.
A set of contiguous slices through the heart.

## Slide 67: Dimensions
Space
5
In-Stack Position
Stack ID = 1
4
3
2
1
Dimension Index Pointers:
Stack ID
In-Stack Position

## Slide 68
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space
Time
5
In-Stack Position
Stack ID = 1
4
3
2
1
5
In-Stack Position
Stack ID = 1
4
3
2
1
Add dimension of time (delay time from R-wave).
Sets of contiguous slices throughout cardiac cycle.

## Slide 69
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (1)
Time (2)
Dimension Index Pointers:
Stack ID
In-Stack Position
Temporal Position Index
5
In-Stack Position
Stack ID = 1
4
3
2
1
5
In-Stack Position
Stack ID = 1
4
3
2
1

## Slide 70
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (1)
Time (2)
1
\
5
\
2
Dimension Index Values
Dimension Index Pointers:
Stack ID
In-Stack Position
Temporal Position Index
5
In-Stack Position
Stack ID = 1
4
3
2
1
5
In-Stack Position
Stack ID = 1
4
3
2
1

## Slide 71
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (1)
Time (2)
1
\
5
\
2
Dimension Index Values
Dimension Index Pointers:
Stack ID
In-Stack Position
Temporal Position Index
5
1\5\1
In-Stack Position
Stack ID = 1
4
1\4\1
3
1\3\1
2
1\2\1
1
1\1\1
5
1\5\2
In-Stack Position
Stack ID = 1
4
1\4\2
3
1\3\2
2
1\2\2
1
1\1\2

## Slide 72
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
1
\
5
Dimension Index Values
Dimension Index Pointers:
Temporal Position Index
Stack ID
In-Stack Position
5
1\1\5
In-Stack Position
Stack ID = 1
4
1\1\4
3
1\1\3
2
1\1\2
1
1\1\1
5
2\1\5
In-Stack Position
Stack ID = 1
4
2\1\4
3
2\1\3
2
2\1\2
1
2\1\1

## Slide 73
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
1
\
5
Dimension Index Values
Dimension Index Pointers:
Trigger Delay Time
Stack ID
In-Stack Position
5
1\1\5
In-Stack Position
Stack ID = 1
4
1\1\4
3
1\1\3
2
1\1\2
1
1\1\1
5
2\1\5
In-Stack Position
Stack ID = 1
4
2\1\4
3
2\1\3
2
2\1\2
1
2\1\1

## Slide 74: Dimension Features
Description of dimensions separate from their indices
  dimensions are described once
  indices within dimensions are encoded per-frame
  a dimension may have only a single index value
Receiving application only needs to follow the index values
  does NOT need to “understand” the attribute values
  does NOT need to select or sort by attribute value
  dimensions can be entire functional groups
  can be private attributes or private functional groups

## Slide 75: Dimension Applications
Define sort order for simple viewing
  replace dependence on encoded order, Instance #
Partitioning of frames for hanging
  hanging protocol can match pattern of Dimensions
Selection of frames that constitute a
  volume in space
  temporal sequence
  contrast administration phase
  acquisition parameter, e.g. data type
  combinations of the above

## Slide 76: Dimensions in IHE DIFF, PERF

## Slide 77: Quantitation of Size and Value
Quantitation of pixel size
  measure distance, area, volume
  Pixel Measures functional group
Quantitation of pixel values
  measure intensity, velocity, etc.
  Real World Value Map functional group
  top level data set Rescale values not used
  separate from rendering pipeline

## Slide 78: Real World Value Mapping
Value
Unit
Stored
Values
Real
Value
LUT
VOI
LUT
P
LUT
Display
Real world
value
Modality
LUT
Measurement
Units Code
Sequence
(0040,08EA)
Real World
Value LUT
Data
(0040,9212)
Real World
Value Intercept
and Slope
attributes
or

## Slide 79
In this case values included; linear, identity mapping
Output of mapping; with code meaning of units
Coordinates of current cursor position
Cursor over pixel
Stored pixel value

## Slide 80: Real World Values
Separate from rendering pipeline
  may be linear or non-linear (LUT)
  may be multiple mappings into different units of different range of values
May be different for each frame
  not different “regions” of same frame
Coded Units
  e.g., ([hnsf'U], UCUM, "Hounsfield unit")
Quantity (CP 1387)
  e.g., (122713, DCM, "Attenuation Coefficient")

## Slide 81: Enhanced US Volume Blending and Display Pipeline

## Slide 82: Path for Single Data Type

## Slide 83: But when ?
Modality
PACS

## Slide 84: PACS Enhanced MF Support
Store and regurgitate (and archive) ?
“Basic” display?
  scroll through frames in encoded order
“Advanced” display?
  sort/scroll by dimensions, stacks, temporal positions
  synchronized scrolling
  measure size & intensity using functional groups
“3D” display?
  3D cursors
  MPR
  volume rendering
CD/DVD viewer support (only basic required in IHE BIR)
IHE DIFF, PERF, DBT profile support

## Slide 85: PACS to PACS (or VNA) with Legacy DICOM Object Conversion
Modality
Modality
Workstations
PACS
Convert SF -> MF
Convert MF -> SF
Classic SF
Legacy Converted MF
True Enhanced MF
PACS
Convert SF -> MF
Convert MF -> SF

## Slide 86: Enhanced MF for Research
Easier to keep data for a single “experiment” organized
Slices all together in one object
Standard volume geometry
Can explicitly describe dimensions
  generic: space, time, cardiac cycle position
  specific: standard or private
Supported by secondary capture
  e.g., for novel modalities
  as of CP 600

## Slide 87: Enhanced MF Intermediates
To join processing pipeline components
  without loosing “composite context” (patient, …)
Same arguments apply as for acquisition
  private frame descriptions and dimensions
  e.g., real and imaginary frames
Major gap is the absence of floating point pixel data representations
  OF, OD value representation (IEEE float 32, 64)
  not defined for Pixel Data (7FE0,0010)
  not supported by toolkits for Pixel Data
  being addressed in new Sup 172 Parametric Map

## Slide 88: DICOM & Quantitative Results
Quantitative analysis need not be proprietary
  standard and interoperable results encoding
Quantitative analysis need not be a “dead end”
  can just transcribe or cut-and-paste numbers into a dictated or plain text report
    but … pre-populated “merge” fields created from structured input provide a productivity and quality gain
  can indeed save pretty tables & graphics as a PDF
    but … much better to be able to re-use structure, numbers, codes next time for comparison, searching, mining and basis for quality improvement metrics
DICOM appropriate when results image-related
  e.g., from Regions of Interest (ROIs)

## Slide 89: DICOM Encoding of ROIs
Private elements
  evil & must be stopped
Curves in image
  weak semantics, old, retired
Overlays in image
  weak semantics
Presentation States
  weak semantics, PACS favorite
Structured Reports
  best choice, but more work
RT Structure Sets
  coordinates only
Segmentations
  per-voxel ROIs; use with SR
Date | Volume | Auto LD | Auto SD
20021207 | 27080 | 49 | 27
… | … | … | …

## Slide 90: DICOM Structured Reports
Hierarchical structure
  codes, numbers, coordinates, image references, etc.
Flexibility is constrained by templates
  just as XML is constrained by DTD or Schema
Standard DICOM binary representation
  easily stored in PACS, though visualization remains challenging
  easily transcoded to XML, JSON, SQL, CSV for processing
Widely used in existing quantitative modalities
  echo-cardiography, obstetric ultrasound

## Slide 91: SR – Questions + Answers
Basic structure is name-value pair
  name is the “question” (code)
  value is the “answer” (text, code, numeric, etc.)
Codes leverage external lexicons
  SNOMED, LOINC, … as well as DCM codes
Different style choices possible, e.g.
  (M-54000,SRT,“Necrosis”) = (G-A203,SRT,“Present”)
  (F-00005,SRT,“Finding”) = (M-54000,SRT,“Necrosis”)
Template of questions & value sets
  populated by human (pick lists from value sets)
  image processing (e.g., signal, pattern detected)
  rule based (e.g., too small to measure)

## Slide 92: DICOM SR – details inside

## Slide 93: DICOM SR – as visualized
Date | Volume | Auto LD | Auto SD
20021207 | 27080 | 49 | 27
… | … | … | …

## Slide 94: DICOM RT Structure Sets
Simple structure
  focus is iso-contour 3D coordinates of regions to treat & spare
  very limited semantics
  no standard or extensible measurements beyond simple volume
Standard DICOM binary representation
  easily transcoded to other DICOM objects like SR or PS
  if 3D (patient-relative) to 2D (image-relative) coordinate mapping is available (e.g., via source images or an SR image library)
Widely used in existing RT & non-RT workstations
  also understood by many academic software tools

## Slide 95: DICOM Presentation States
Intended to preserve appearance
  grayscale pipeline (window)
  spatial transformation (pan/zoom)
  annotation (text, overlays, vector graphics)
  color and pseudo-color versions
Lack semantics
  what does the text “mean”? (need NLP?)
  which graphic is it associated with?
Overall, a poor choice for quantitative results
  but may be all that is available in many PACS (to create & view)

## Slide 96: Parametric Maps
Foster N L et al. Brain 2007;130:2616-2635
Meyer P T et al. J Neurol Neurosurg Psychiatry 2003;74:471-478

## Slide 97: Label Maps & Segmentations
Brewer J et al. AJNR 2009; 30:578-580

## Slide 98: Encapsulated PDF

## Slide 99: Parametric & Label Maps
Per-voxel encoding of numeric or label values
Ordinary images but not just “pretty pictures”
  modality-specific or secondary capture; single or multi-frame
  not just a PDF-like “static” secondary capture color screen shot
Segmentations (label maps)
  binary, probability, fractional occupancy
  multiple segments (multiple labels)
Parametric maps currently limited to integer values
  can provide (linear) rescaling to floats (usable by any viewer)
  Sup 172 extension to floating point voxels (or private SOP Class)
Leave “fusion” (superimposition) to application
  Blending Presentation State to specify what to fuse
  e.g., segment/parameter + CT or MR (like PET SUV + CT)

## Slide 100: Registration & Fiducials
Mapping between 3D coordinates
  DICOM Registration – rigid matrix
  DICOM Deformable Registration
Location of specific points
  DICOM Fiducial
Used to save manual or automated results
  save application state for further work later
  re-use for other purposes (e.g., sync’d scrolling)

## Slide 101: DICOM Real World Value Maps
“Standalone” objects
  i.e., separate from images (not just in them)
Separate pipelines based on pixels
  what to show on the display
  what the pixel (voxel) “means”
e.g., MR pixel values
  signal intensity windowed for display
  mapped to physical unit (e.g. velocity for phase contrast)
DICOM encoding
  linear equation or LUT, applied to all or sub-set of range
  point operation (all voxels) (unlike US Region Calibration)

## Slide 102: Quantitative Objects Together
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 103: Summary
Background of DICOM IODs for storage
“Enhanced Multi-frame” family of objects – principles
Performance, compression, organization, attributes
Geometry, coded anatomy, hanging, timing, data type
Functional groups, dimensions, stack, temporal index
Real world value maps and display pipeline
PACS support for Enhanced Multi-frame
Legacy conversion
Quantitation and DICOM non-image objects for ROIs